## Slide 1
The History of Propane The Discovery
In 1910, Dr. Walter Snelling a chemist and explosives expert for the U.S. Bureau of Mines, was contacted to investigate vapors coming from a gasoline tank on a newly purchased Ford Model T.
Dr. Snelling filled a glass jug with the gasoline and discovered on his way back to the lab that volatile vapors were forming in the jug, causing its cork to repeatedly pop out. After dividing the gas into its liquid and gaseous components, he learned that propane was one component of the liquefied gas mixture

## Slide 2: Propane is Processed from two sources:
              20% Crude Oil
              80% “wet” Natural Gas
                HD 5 Propane is a mixture of Butane and Propane.
                Inside a container there is 100% gas no air.

## Slide 3: LP-Gas Characteristics
Will expand when heat is applied
Non-toxic, but presents possible
inhalation hazards
When released in a confined space, propane can displace oxygen
Propane weighs 4-1/4 lbs. per gallon

## Slide 4
Characteristics of
LP-Gas
Stored as a Liquid
· Colorless
· Tasteless
· Usually Odorless
    vaporizes when exposed to
the atmosphere

## Slide 5
  Propane is odorless until an
odorant called Ethyl Mercaptan
is added at 1 pound per 10,000
gallons (one drop per 100-pound
cylinder)
This warning agent can be detected
by a distinct “rotten eggs” odor

## Slide 6
At any temperature above -44 F propane will begin to boil off into a vapor and therefore needs
to be stored in a closed container.
Leaking liquid propane coming in contact with your skin can cause severe frost bite.
LP is stored and handled as a liquid when under pressure inside an LP-Gas Container
Notes: Show Propane Beaker hot plate

## Slide 7
Ratio of Expansion
Liquid to Vapor - 270 to 1
Propane stored as a liquid
Propane stored as a gas

## Slide 8: Expansion
It is this expansion factor which makes it more economical to transport and store large quantities of gaseous fuel in a small container.
At any temperature above -44 F propane will begin to boil off into a vapor and therefore needs
to be stored in a closed container.
Leaking liquid propane coming in contact with your skin can cause severe frost bite.
LP is stored and handled as a liquid when under pressure inside an LP-Gas Container
Natural gas does not work in this way.

## Slide 9
The Many Uses for Propane:
For the Home
Heat• Vehicles • Clothes Drying Water Heating •Fireplace (Aesthetics) • Cooking •
Lighting •Grilling •Generator •Pool Heating • Propane Torch
• Weed Eating • Mosquito control • Garage/Space Heating
• Portable heating • Lawn Mower • Refrigeration

## Slide 10
For the Farm
• Vehicles• Farm Equipment
• Crop drying• Crop Cultivation
• Pest Control• Propane Cannon (Noise for Pests)
• Tractors• Animal Husbandry
• Heating Barns• Refrigeration